## Slide 1: Electricity -- The Basics!

## Slide 2: Interactions of Charge Centers

## Slide 3: Basic Electrical Relationships
Coulomb -- a unit of charge
1 coulomb = 6.2×1018 elementary charges
Coulomb’s Law
The electrical analog of velocity is current:
The electrical analog of force is electromotive force (E):
(force in N)

## Slide 4: Electrical Potential
Potential to do work is always measured relative to some reference state. In electricity, zero potential (ground) can be viewed as an electrically neutral location that is an infinite sink for charge (next slide).

## Slide 5: Movement of Charges
A good analogy is the expansion of gases into larger containers -- although the proximate cause of the expansion is quite different!

## Slide 6: Resistance
Resistance is that which limits current flow (for a given potential) and consumes electrical energy (resistances convert electrical energy to other forms such as heat).
R (resistance) is measured in ohms (W);
G (conductance, its inverse) is measured in siemens (S).

## Slide 7: A Purely Resistive Circuit
Which way does the current flow?

## Slide 8: Fluid Analog to Resistance, Current and Potential
"ResistanceHydraulicAnalogy" by Sbyrnes321 - Own work. Licensed under CC0 via Commons - https://commons.wikimedia.org/wiki/File:ResistanceHydraulicAnalogy.svg#/media/File:ResistanceHydraulicAnalogy.svg
Pressure difference is potential difference
Flow is like current

## Slide 9: Series and Parallel Resistive Circuits
Can you draw an analogy to these circuits using water flow?

## Slide 10: Capacitance
Capacitance is the ability to store electrical charge; the larger the capacitance, the greater that ability.
Capacitors (ideal ones) do not consume energy – whatever energy they store can be retrieved.

## Slide 11: Capacitance
Energy storage -- the electrical analog of elasticity

## Slide 12: A Purely Capacitive Circuit

## Slide 13: Equilibrium in a capacitive circuit

## Slide 14: RC Circuits
RC (resistive-capacitive) circuits both store and consume energy.
These will be important in our discussions of membrane potentials, especially ones that vary and move.

## Slide 15: An RC Circuit

## Slide 16: The Time Constant, t
A measure of the time needed to charge an RC circuit.
t = RC
If t = t then 1-(1/e) = 1-(1/2.7)
= 1 – 0.37
= 0.63

## Slide 17: The Effect of the Time Constant